Examples of calculating Coverage using the adopted regulations in Amendment #621  1/5/11

40,000 Square foot lot

Total coverage of 25% max = 10,000 square feet

Building coverage of 15% max = 6,000 square feet

If the building coverage is maxed out, there is 4,000 square feet left for drives, pools, patios, etc.

Example:

Propose 3,000 square feet of patios and decks, all permeable.  Approved permeable decks and patios count at 2/3 the total coverage.

3,000 X .66 = 1980 square feet coverage for patios and decks count in coverage but get 3,000 square feet on the ground.

In addition, 500 square feet can count in the bonus patio and deck coverage. (based on 2%  of the net lot area or 500 feet, whichever is less.)

4,000 square feet for drives, pool, patios, decks to count in total coverage.

+ 500 square feet patio and deck bonus

4,500 square feet

-1,980 patio and deck coverage

2,520 square feet left for pool, drive, open porch, etc.

20,000 Square Foot Lot

Total coverage of 25% max = 5,000 square feet

Building coverage of 15% max = 3,000 square feet

If the building coverage is maxed out, there is 2,000 square feet left for drives, pools, patios, etc.

Example:

Propose 800 square feet of patios and decks, all permeable.  Approved permeable decks and patios count at 2/3 the total coverage.

800 X .66 = 528 square feet coverage for patios and decks counted in coverage but get 800 square feet on the ground.

In addition,  400  square feet can count in the bonus patio, terrace and deck coverage. (based on 2%  of the net lot area or 500 feet, whichever is less.)

2,000 square feet for drives, pool, patios, terraces, decks to count in total coverage.

+ 400 square feet patio and deck bonus

2,400 square feet

-  528 patio and deck coverage

1,572 square feet left for pool, drive, open porch, etc.

20,000 Square foot Lot  - Alternate Plan

Total coverage of 25% max = 5,000 square feet

Building coverage of 15% max = 3,000 square feet

If the building coverage is maxed out, there is 2,000 square feet left for drives, pools, patios, etc.

Example:

Propose a drive, pool and open porches (part of total coverage)

Propose 300  square feet patio, all permeable.  Approved permeable decks and patios count at 2/3 the total coverage.

300 X .66 = 198 square feet coverage for patios counted in coverage but get 300 square feet on the ground.

In addition,  all of the 198  square feet can count in the bonus patio and deck coverage. (based on 2%  of the net lot area ( 400 square feet)  or 500 square feet, whichever is less.)  The additional 102 square feet of total coverage can be used at another time for patios, terraces or decks only.

2,000 square feet for drives, pool, patios, decks to count in total coverage.

+ 198 square feet patio and deck bonus at this time (102 square feet left for another time)

2,198 square feet

-  198 patio and deck coverage

2,000 square feet left for pool, drive, open porch, etc.

elPZCoverageCalcNewAmendment